## Slide 1
Edge Counter Arc Pairs

## Slide 2
Step 1
Add new tool – Halcon Script – in your inspection program.

## Slide 3
Step 2
Click „Browse” and choose „EdgeCounterArcPairs.hdev” file.

## Slide 4
Step 3
Set the Arc Center position (X and Y), Arc Radius, Arc Angle Start and Arc Angle Extent.
If Arc Angle Extent will be greater than 0 counterclockwise orientation of the arc will be generated.
If Arc Angle Extent will be lesser than 0 clockwise orientation of the arc will be generated.
Arc will be displayed as red element on the image.

## Slide 5
Step 3
Adjust edge parameters:
AmplitudeThreshold – minimum edge contrast
RoidWidthLength – length of the line perpendicular to the generated Arc
Sigma – smoothing

## Slide 6
Step 4
You can also specify the edge Transition:
Positive – only light pairs will be found
Negative – only dark pairs will be found
All – pairs with both polarity will be found

## Slide 7
Step 5
You can also Select the edges:
First – only first pair will be found
Last – only last pair will be found
All – all of the pairs will be found

## Slide 8
Step 6
Set the number of pairs that you want to get as an output.
Found pairs will be displayed as Crosses on the image.

## Slide 9
Step 7
Available output parameters:
NumberOfPairs – number of found pairs
FirstPositionX (n) – X position of the first edge of the (n) found pair
FirstPositionY (n) – Y position of the first edge of the (n) found pair
SecondPositionX (n) – X position of the second edge of the (n) found pair
SecondPositionY (n) – Y position of the second edge of the (n) found pair
IntraDistance (n) – distance between first and second edge in (n) found pair
InterDistance (n) – distance between second edge in (n) pair and first edge in (n+1) pair
FirstPositionXCalibrated (n) – X position of the first edge of the (n) found pair after calibration
FirstPositionYCalibrated (n) – Y position of the first edge of the (n) found pair after calibration
SecondPositionXCalibrated (n) – X position of the second edge of the (n) found pair after calibration
SecondPositionYCalibrated (n) – Y position of the second edge of the (n) found pair after calibration
IntraDistanceCalibrated (n) – distance between first and second edge in (n) found pair after calibration
InterDistanceCalibrated (n) – distance between second edge in (n) pair and first edge in (n+1) pair after calibration

## Slide 10
Step 8
Calibrated output parameters have proper values if the UseCalibration variable is checked and calibration data is available.

## Slide 11
Step 9
It is also possible to use locator from previous tools – in InputImage choose output image from locator tool (for example Find object tool).